SECTION 07 46 49

SYNTHETIC SHAKE SIDING

This section includes editing notes to assist the user in editing the section to suit project requirements. These notes are included as hidden text, and can be revealed or hidden by the following method in Microsoft Word:

Display the FILE tab on the ribbon, click OPTIONS, then DISPLAY. Select or deselect HIDDEN TEXT.

This guide specification section has been prepared by DaVinci Roofscapes, LLC for use in the preparation of a project specification section covering synthetic shake siding.

The following should be noted in using this specification:

Hypertext links to specific websites are included after manufacturer names and names of organizations whose standards are referenced within the text, to assist in product selection and further research. Hypertext links are contained in parenthesis and shown in blue, e.g.:

(www.astm.org)

Items requiring user input are enclosed within brackets and included as red text, e.g.:

Section [09 00 00] [__ __ __.]

Optional paragraphs are separated by an "OR" statement included as red text, e.g.:

**** OR ****

Sustainable requirements are included for projects requiring LEED certification, and are included as green text. For additional information on LEED, visit the U.S. Green Building Council website at www.usgbc.org.

For assistance on the use of the products in this section, contact DaVinci Roofscapes, LLC by calling 800-DAVINCI, by email at mstone@davinciroofscapoes.com, or visit their website at www.davinciroofscapes.com.

- GENERAL

  - SUMMARY

Edit the following to include only those items specified in this section.

    - Section Includes:

      - Synthetic shake siding, moisture barrier, flashings, fasteners, and accessories.

Coordinate the following with other sections in the Project Manual.

    - Related Requirements:

      - Division 01 - General Requirements: Administrative, procedural, and temporary work requirements.

      - Section [07 62 00 - Sheet Metal Flashing and Trim.] [__ __ __ - _______.]

      - Section [07 92 00 - Joint Sealers.] [__ __ __ - _______.]

  - REFERENCES

Edit the following to include only those references used elsewhere in this section.

    - American Society for Testing and Materials (ASTM) (www.astm.org):

      - D226/D226M - Standard Specification for Asphalt-Saturated Organic Felt Used in Roofing and Waterproofing.

      - D7254 - Standard Specification for Polypropylene (PP) Siding.

      - G21 - Standard Practice for Determining Resistance of Synthetic Polymeric Materials to Fungi.

    - California Building Code (http://www.fire.ca.gov) (CBC) SFM Standard 12-7A-1 - Fire Resistive Standard for Exterior Wall Siding and Sheathing.

  - ADMINISTRATIVE REQUIREMENTS

Retain the following for a pre-installation conference to review the work of this section prior to installation.

    - Pre-Installation Conference:

      - Convene at Project site [2] [__] weeks prior to beginning work of this Section.

      - Attendance: [Architect,] [Contractor,] [Construction Manager,] installer, and related trades.

      - Review and discuss:

        - Installation procedures and manufacturer's recommendations.

        - Safety procedures.

        - Coordination with installation of other work.

        - Availability of materials.

        - Preparation and approval of substrate and penetrations through siding.

        - Other items related to successful execution of work.

  - SUBMITTALS

Retain the following for submittals requiring the Design Professional’s review.

    - Action Submittals:

      - Shop Drawings: Show siding layout, method of attachment, flashings, trim, intersections with adjacent materials, and other installation details.

      - Product Data: Manufacturer's data sheets on each product including:

        - Siding, moisture barrier, flashings, fasteners, and accessories:

          - Indicate composition, properties, and dimensions.

          - Show compliance with specified requirements.

        - Preparation instructions and recommendations.

        - Storage and handling requirements and recommendations.

        - Installation methods.

      - Samples:

        - Selection Samples: Two sets of color chips representing manufacturer's full range of available colors and surface textures.

        - Verification Samples: After selection, submit two samples representing actual product, color, and texture.

Retain the following for projects requiring sustainable documentation.

    - Sustainable Design Submittals: Refer to Division 01.

Retain the following for extra materials for the Owner's maintenance after completion.

    - Maintenance Material Submittals: Provide [__] square feet of extra siding.

  - QUALITY ASSURANCE

Retain the following if required; edit to suit project requirements.

    - Manufacturer Qualifications: Company specializing in manufacture of synthetic shingles.

    - Installer Qualifications: Minimum [3] [__] years experience in work of this Section.

Retain the following for field or shop mockups for review of construction, coordination of work of multiple sections, testing, or observation of operation.

    - Mockup:

      - Provide mockup of siding, moisture barrier, and related flashings.

      - Size: Minimum [8 x 8] [__ x __] feet.

      - Locate [where directed.] [____.]

      - Approved mockup [may] [may not] remain as part of the Work.

  - DELIVERY, STORAGE AND HANDLING

    - Ship siding in bundles:

      - Collate in sequence of widths and colors as required for selected color blend.

      - Assemble bundles so that sorting at job site is not required.

    - Deliver siding to site in manufacturer's unopened, labeled bundles.

      - Verify quantities and condition upon delivery.

      - Remove damaged products from site.

    - Store products in protected environment, off ground, protected moisture, traffic, and construction activities.

    - Store siding flat. Do not store on site for prolonged period.

    - Store products at temperature between 40 and 120 degrees F (4 degrees C and 49 degrees C).

    - Store and dispose of solvent-based materials, and materials used with solvent-based materials, in accordance with requirements of authorities having jurisdiction.

  - SITE CONDITIONS

    - Environmental Requirements:

      - Observe manufacturer’s temperature, humidity, and moisture limits.

      - Do not install products under environmental conditions outside manufacturer's absolute limits.

  - WARRANTIES

    - Furnish manufacturer’s 50 years warranty against breakage and deterioration resulting in leaks under normal weather and use conditions.

    - Furnish installer's 2 years total siding system warranty against water penetration, including moisture barrier, flashings, trim, and other components.

- PRODUCTS

  - MANUFACTURERS

    - Acceptable Manufacturer: DaVinci Roofscapes, LLC, 800-DAVINCI, www.davinciroofscapes.com.

Edit the following to indicate whether or not substitutions will be permitted for the products in this section.

    - Substitutions: [Refer to Division 01.] [Not permitted.]

  - MATERIALS

    - Performance Requirements: Manufactured synthetic siding attached to structural substrate to form weather tight wall envelope with no measurable water penetration.

    - Synthetic Shake Siding:

      - Description: Lightweight, synthetic shake siding with appearance, color, texture, and thickness of natural wood shakes.

      - Product: Hand Split Shake.

      - Material: Engineered polymer formulated from 100 percent virgin plastic resins; recycled materials not acceptable.

      - Performance characteristics:

        - Certified to ASTM D7254.

        - Fire resistance: Comply with Conditions of Acceptance of CBC SFM 12-7A-1.

        - Water absorption: 0.18 percent by weight, tested to ASTM D471.

        - Impact resistance: Class 4, tested to UL 2218.

        - Nail pull through resistance: 138 foot-pounds at 72 degree F (187 joules at 22 degrees C) and 166 foot-pounds at 32 degrees F (225 joules at 0 degrees C), tested to ASTM D3462/D3462M.

        - Freeze-thaw resistance: No crazing, cracking, delamination of coating, or other deleterious surface changes after one month exposure with temperature cycled from minus 40 to plus 180 degrees F (0 degrees to 82 degrees C) in 22 hours, tested to ICC  ES Acceptance Criteria AC07 Section 4.9.

        - Accelerated weathering: Little change after 2,500 hours exposure to ultraviolet radiation, elevated temperature, moisture, and thermal shock.

        - Fungus resistance: No algae growth when inoculated with blue green algae in warm, damp environment for 4 to 6 weeks, tested to ASTM G21.

      - Installed weight: [6 inch (152 mm) exposure: 410 pounds per 100 square feet (22.3 kg/sq. m).] [7 inch (178 mm) exposure: 360 pounds per 100 square feet (19.5 kg/sq. m).] [8 inch (203 mm) exposure: 313 pounds per 100 square feet (16.5 kg/sq. m).]

      - Profile:

        - Rectangular shape with exposed-to-view upper surface and edges textured to resemble natural wood shake.

        - Underside formed with reinforcing ribs.

      - Size:

        - Thickness: 5/8 inch (16 mm) at butt end.

        - Length: 18 inches (457 mm).

        - Width: [8] [10] inches ([203] [254] mm).

        - Starter: 12 inches (305 mm) long x same width as shakes.

      - Markings: Form siding with markings on upper surface to indicate nailing locations and provide alignment guidelines for different exposure lengths.

      - Color:

        - Colors comparable to natural wood shakes.

        - Provide internal ultraviolet stabilizers.

      - Siding blend: [Aged Cedar.] [Black Oak.] [Mossy Cedar.] [Slate Blue.] [Taupe.] [Bark.] [Sage.] [Granite.]

  - ACCESSORIES

    - Underlayment: ASTM D226/D226M, Type II, No. 30 non-perforated saturated asphalt felt.

Copper is recommended flashing material although 26 gage galvanized steel can also be used.

    - Flashing:

      - Fabricate from sheet to profiles and dimensions indicated on Drawings and approved Shop Drawings, in accordance with Section [07 60 00.] [__ __ __.]

      - Material: [16 ounce copper.] [26 gage (0.455 mm) galvanized steel.]

      - Linear components: Form in longest possible lengths, 8 feet (2.5 m) minimum.

DaVinci Roofscapes, LLC recommends copper nails be used to attach siding. Acceptable alternatives are stainless steel and hot-dipped galvanized.

    - Fasteners:

      - 3/8 inch (9.5 mm) flat head nails, 1-1/2 inches (38 mm) long.

      - Material: [Copper.] [Stainless steel.] [Hot-dipped galvanized steel.]

- EXECUTION

  - EXAMINATION

    - Inspect wall framing and substrate.

      - Verify that wall is complete, rigid, and braced, and that sheathing is securely fastened.

      - Verify that sheathing is clean, dry, and ready to receive siding.

      - Remove dirt, loose fasteners, and protrusions from wall surface.

  - INSTALLATION - UNDERLAYMENT

    - Install one ply asphalt felt over full wall area, with ends weather lapped minimum 4 inches (102 mm). Nail in place with nails spaced in accordance with manufacturer's recommendations.

  - FLASHING INSTALLATION

    - Install metal flashings at penetrations and intersections with adjacent surfaces, in accordance with Section [07 62 00.] [__ __ __.]

    - Weather lap joints minimum 2 inches (52 mm) and seal with sealant as specified in Section [07 92 00.] [__ __ __.]

    - Secure in place with clips, nails, or other fasteners.

  - SIDING INSTALLATION

    - Install siding in accordance with manufacturer's instructions and approved Shop Drawings.

    - Accurately lay out siding. Ensure that edges are parallel and perpendicular to building lines. Lay out work to avoid cutting siding.

      - If cutting is required, place siding so that cut edge is not exposed.

      - Use circular saw or straight edge and utility knife if cuts are necessary.

    - Exposure: Install siding in straight pattern with [6 inch (152 mm)] [7 inch (178 mm)] [8 inch (203 mm] exposure and bottom shingle edges [evenly aligned.] [staggered 1 inch (25 mm) in adjacent rows.]

    - Spacing: Provide 3/16 to 3/8 inch (4.76 to 9.5 mm) gap between adjacent shakes.

    - Stagger joints in one course minimum 1-1/2 inches (38 mm) from joints in course below.

    - Fastening: Attach each shake to substrate with two nails:

      - Place nails at locations indicated on shakes.

      - Ensure full penetration but do not overdrive nails.

      - Do not nail at an angle.

      - Ensure that nail head is flush with siding surface.

  - FIELD QUALITY CONTROL

    - Inspect units as they are installed. Do not install cracked, broken, twisted, curled, or otherwise damaged units.

    - As work progresses, exercise care not to scratch or mar installed siding. Replace damaged siding.

    - After approximately 200 units have been installed, inspect wall from ground. Verify proper layout and appearance. Repeat inspection every 200 shingles.

    - Visually inspect completed installation for weathertight condition.

  - PROTECTION

    - Protect installed siding until completion of Project.

  - ADJUSTING

    - Replace damaged siding prior to Substantial Completion.

END OF SECTION